## Slide 1: Chapter 30 Current and Resistance
Chapter Goal: To learn how and why charge moves through a conductor as what we call a current.
Slide 30-2

## Slide 2: Chapter 30 Preview
Slide 30-3

## Slide 3
Chapter 30 Preview
Slide 30-4

## Slide 4
Chapter 30 Preview
Slide 30-5

## Slide 5
Chapter 30 Preview
Slide 30-6

## Slide 6
Chapter 30 Preview
Slide 30-7

## Slide 7
Chapter 30 Preview
Slide 30-8

## Slide 8
Chapter 30 Preview
Slide 30-9

## Slide 9: Electric Current
How does a capacitor get discharged?
Figure (a) shows a charged capacitor in equilibrium.
Figure (b) shows a wire discharging the capacitor.
As the capacitor is discharging, there is a current in the wire.
Slide 30-20

## Slide 10
When a current is flowing, the conductors are not in electrostatic equilibrium.
Though you cannot see current directly, there are certain indicators that current is present in a wire.
Electric Current
Slide 30-21

## Slide 11: Charge Carriers
The outer electrons of metal atoms are only weakly bound to the nuclei.
In a metal, the outer electrons become detached from their parent nuclei to form a fluid-like sea of electrons that can move through the solid.
Electrons are the charge carriers in metals.
Slide 30-22

## Slide 12: The Electron Current
We define the electron current ie to be the number of electrons per second that pass through a cross section of the conductor.
The number Ne of electrons that pass through the cross section during the time interval t is
Slide 30-23

## Slide 13: The Electron Current
If the number density of conduction electrons is ne, then the total number of electrons in the shaded cylinder is
Ne  neV  V=Volume
 neAx
 neAvdt
So the electron current is:
Slide 30-24

## Slide 14: The Electron Density
In most metals, each atom contributes one valence electron to the sea of electrons.
Thus the number of conduction electrons ne is the same as the number of atoms per cubic meter.
Slide 30-27

## Slide 15: Discharging a Capacitor
How long should it take to discharge this capacitor?
A typical drift speed of electron current through a wire is vd  104 m/s.
At this rate, it would take an electron about 2000 s (over half an hour) to travel 20 cm.
But real capacitors discharge almost instantaneously!
What’s wrong with our calculation?
Slide 30-29

## Slide 16
The wire is already full of electrons!
We don’t have to wait for electrons to move all the way through the wire from one plate to another.
We just need to slightly rearrange the charges on the plates and in the wire.
Discharging a Capacitor
Slide 30-30

## Slide 17: Creating a Current
A book on a table will slow down and stop unless you continue pushing.
Analogously, the sea of electrons will slow down and stop unless you continue pushing with an electric field.
Slide 30-31

## Slide 18: Establishing the Electric Field in a Wire
The figure shows two metal wires attached to the plates of a charged capacitor.
This is an electrostatic situation.
What will happen if we connect the bottom ends of the wires together?
Slide 30-32

## Slide 19
Within a very brief interval of time (109 s) of connecting the wires, the sea of electrons shifts slightly.
The surface charge is rearranged into a nonuniform distribution, as shown in the figure.
Establishing the Electric Field in a Wire
Slide 30-33

## Slide 20
The nonuniform distribution of surface charges along a wire creates a net electric field inside the wire that points from the more positive end toward the more negative end of the wire.
This is the internal electric field that pushes the electron current through the wire.
Establishing the Electric Field in a Wire
Slide 30-34

## Slide 21: A Model of Conduction
Within a conductor in electrostatic equilibrium, there is no electric field.
In this case, an electron bounces back and forth between collisions, but its average velocity is zero.
Slide 30-37

## Slide 22
In the presence of an electric field, the electric force causes electrons to move along parabolic trajectories between collisions.
Because of the curvature of the trajectories, there is a slow net motion in the “downhill” direction.
A Model of Conduction
Slide 30-38

## Slide 23
The graph shows the speed of an electron during multiple collisions.
The average drift speed is
A Model of Conduction
Slide 30-39

## Slide 24: Electron Current
The electric field strength E in a wire of cross-section A causes an electron current.
The electron density ne and the mean time between collisions  are properties of the metal.
The electron current is directly proportional to the electric field strength.
Slide 30-40
Electron Current

## Slide 25: Current
If Q is the total amount of charge that has moved past a point in a wire, we define the current I in the wire to be the rate of charge flow:
The SI unit for current is the coulomb per second, which is called the ampere.
1 ampere = 1 A = 1 C/s.
The conventional current I and the electron current ie are related by
Slide 30-43
Current
current is the rate at which charge flows

## Slide 26: Example 30.4 The Current in a Copper Wire
Slide 30-46

## Slide 27: Current
Note that the direction of the current I in a metal is opposite to the direction of the electron current ie.
Slide 30-47

## Slide 28: The Current Density in a Wire
The current density J in a wire is the current per square meter of cross section:
The current density has units of A/m2.
Slide 30-48
The Current Density in a Wire

## Slide 29: Conservation of Current
The figure shows two lightbulbs in the wire connecting two charged capacitor plates.
As the capacitor discharges, the current through both bulbs is exactly the same!
The rate of electrons leaving a lightbulb (or any other device) is exactly the same as the rate of electrons entering the lightbulb.
Slide 30-52

## Slide 30
Conservation of Current
Slide 30-53

## Slide 31: Kirchhoff’s Junction Law
For a junction, the law of conservation of current requires that
where the  symbol means summation.
This basic conservation statement is called Kirchhoff’s junction law.
Slide 30-56

## Slide 32: Conductivity and Resistivity
The conductivity of a material is
Conductivity, like density, characterizes a material as a whole.
The current density J is related to the electric field E by:
The resistivity tells us how reluctantly the electrons move in response to an electric field:
Slide 30-59

## Slide 33: Conductivity and Resistivity
This woman is measuring her percentage body fat by gripping a device that sends a small electric current through her body. Because muscle and fat have different resistivities, the amount of current allows the fat-to-muscle ratio to be determined.
Slide 30-66

## Slide 34
Slide 30-67
Conductivity and Resistivity

## Slide 35: Superconductivity
Superconductors have unusual magnetic properties. Here a small permanent magnet levitates above a disk of the high temperature
superconductor YBa2Cu3O7 that has been cooled to liquid-nitrogen temperature.
In 1911, the Dutch physicist Kamerlingh Onnes discovered that certain materials suddenly and dramatically lose all resistance to current when cooled below a certain temperature.
This complete loss of resistance at low temperatures is called superconductivity.
Slide 30-69

## Slide 36: Resistance and Ohm’s Law
The current density is J  I/A  E/.
So the current is related to V by
The figure shows a section of a conductor in which an electric field E is creating current I by pushing the charge carriers.
The field strength is
Slide 30-70

## Slide 37
The current through a conductor is proportional to the potential difference between its ends.
We define the resistance R of a long, thin conductor of length L and cross-sectional area A to be:
The SI unit of resistance is the ohm.
1 ohm  1   1 V/A.
The current through a conductor is determined by the potential difference V along its length:
Resistance and Ohm’s Law
Slide 30-71

## Slide 38: Batteries and Current
A battery is a source of potential difference Vbat.
The battery creates a potential difference between the ends of the wire.
The potential difference in the wire creates an electric field in the wire.
The electric field pushes a current I through the wire.
The current in the wire is:
I  Vwire/R
Slide 30-74

## Slide 39: Ohm’s Law
Ohm’s law is limited to those materials whose resistance R remains constant—or very nearly so—during use.
The materials to which Ohm’s law applies are called ohmic.
The current through an ohmic material is directly proportional to the potential difference; doubling the potential difference doubles the current.
Metal and other conductors are ohmic devices.
Slide 30-75

## Slide 40: Nonohmic Materials
Some materials and devices are nonohmic, meaning that the current through the device is not directly proportional to the potential difference.
Diodes, batteries, and capacitors are all nonohmic devices.
Slide 30-78

## Slide 41: Battery-Wire-Resistor-Wire Circuit
The figure shows a resistor connected to a battery with current-carrying wires.
Current must be conserved; hence the current I through the resistor is the same as the current in each wire.
The next two slides show how the electric potential varies through the circuit .
Slide 30-79

## Slide 42
Battery-Wire-Resistor-Wire Circuit
Slide 30-80

## Slide 43
Battery-Wire-Resistor-Wire Circuit
Slide 30-81

## Slide 44: Chapter 30 Summary Slides
Slide 30-83

## Slide 45: General Principles
Slide 30-84
General Principles

## Slide 46
General Principles
Slide 30-85

## Slide 47
General Principles
Slide 30-86

## Slide 48: Important Concepts
Slide 30-87
Important Concepts

## Slide 49
Important Concepts
Slide 30-88

## Slide 50
Important Concepts
Slide 30-89